## Slide 1
UAV/机载GPR数据处理深度调研
Processing Workflow · Algorithms · Airborne Constraints · Toolchain
时间：2026-03-06
资料来源：深度调研摘要 + 公开文献
UAV GPR Deep Research

## Slide 2
核心处理流程（标准化管线）
同步/轨迹清洗
time-zero
dewow
gain/AGC/SEC
去背景
(EMA/SVD/RPCA/WNNM)
频带与F-K滤波
迁移成像
速度估计/深度转换
属性/切片成像
注：机载场景需要增加轨迹对齐、运动补偿、等距重采样。
Pipeline

## Slide 3
算法对比结论
背景抑制
SVD / RPCA / WNNM
> EMA
优势：
• 去阴影、保结构
• 目标保真度高
增益策略
SEC > AGC
理由：
• 相位与幅度保真
• 动态范围控制可解释
成像/滤波
F-K + 迁移组合
关键点：
• 时频域噪声隔离
• 速度估计决定成像质量
Algorithm Summary

## Slide 4
机载特性与约束
轨迹对齐
RTK/PPK轨迹 + 航迹插值，要求厘米级同步
等距重采样
将不均匀采样转换为等距道集，稳定F-K/迁移
运动补偿
MoCo修正平台姿态与天线偏移
耦合变化
飞行高度/地表粗糙导致耦合变化，需归一化
姿态稳定
俯仰/横滚影响极化与时延，建议IMU约束
Airborne Constraints

## Slide 5
参数范围建议（机载场景）
中心频率
80–500 MHz（浅层高分辨率 vs 深穿透）
飞行高度
0.5–2.5 m（地表近距以提升耦合）
测线间距
0.1–0.5 m（3D成像建议 ≤0.25 m）
道间距
0.02–0.1 m（与PRF/速度匹配）
采样时间窗
60–200 ns（视介质速度）
速度估计
0.06–0.15 m/ns（土壤/岩土）
增益策略
SEC为主，AGC仅用于可视化
去背景窗口
≥ 30–80 道滑窗，保结构
Parameters

## Slide 6
工具链与实现建议
GPR专业软件
数据处理/集成
• RGPR（R）
• ReflexW
• GPRMax（FDTD仿真）
• GPRPy / gprMax
• MatGPR / GPR-SLICE
• Python: NumPy/Scipy + scikit-image
• 小波/稀疏表示库
• GNSS/IMU融合：RTKLIB
• GIS：QGIS / ArcGIS
• 可视化：Plotly / PyVista
Toolchain

## Slide 7
文献列表（1/2）
https://www.mdpi.com/2072-4292/14/14/3245
https://www.mdpi.com/2072-4292/16/13/2461
https://www.mdpi.com/2072-4292/17/9/1498
https://pmc.ncbi.nlm.nih.gov/articles/PMC10459563/
https://link.springer.com/article/10.1007/s11629-023-8162-y
https://www.preprints.org/manuscript/202401.1034
https://emanuelhuber.github.io/RGPR/02_RGPR_tutorial_basic-GPR-data-processing/
https://www.sandmeier-geo.de/Download/gpr_2d_import_processing.pdf
https://www.mdpi.com/1424-8220/18/10/3422
https://www.mdpi.com/1424-8220/19/17/3807
https://pmc.ncbi.nlm.nih.gov/articles/PMC10255216/
https://www.mdpi.com/2079-9292/9/1/25
https://ieeexplore.ieee.org/document/10197763/
https://www.mdpi.com/2079-9292/10/11/1269
https://core.ac.uk/download/pdf/333722781.pdf
References

## Slide 8
文献列表（2/2）
https://link.springer.com/article/10.1186/s40703-016-0019-6
https://onlinelibrary.wiley.com/doi/10.1155/2014/280738
https://www.sciencedirect.com/science/article/pii/S1877705811054014
https://www.sciencedirect.com/science/article/abs/pii/S0926985121001488
https://www.ajer.org/papers/Vol-12-issue-1/Q1201124133.pdf
https://ieeexplore.ieee.org/document/7105356
https://www.researchgate.net/publication/359995114_Unmanned_Aerial_Vehicle-Based_Ground-Penetrating_Radar_Systems_A_Review
https://www.sphengineering.com/integrated-systems/technologies/gpr
https://www.sphengineering.com/news/ground-versus-uav-based-ground-penetrating-radar-gpr-comparison
https://cdnsciencepub.com/doi/abs/10.1139/dsa-2023-0021
https://www.gprmax.com/
https://github.com/gprMax/gprMax
https://github.com/emanuelhuber/RGPR
https://github.com/NSGeophysics/GPRPy
https://www.sandmeier-geo.de/reflexw.html
https://www.geophysical.com/gpr-slice/
References

## Slide 9
结论
• 机载GPR必须优先解决轨迹对齐与运动补偿
• 背景抑制推荐 SVD/RPCA/WNNM，增益推荐 SEC
• 迁移成像依赖速度估计与F-K滤波，需稳定管线
• 建议工具链：RGPR/ReflexW + Python自动化
Conclusion